## Slide 1: Opening the Black Box
Using Web10G to Uncover the Hidden Side of TCP CC PI Meeting Austin, TX
September 29, 2015
rapier@psc.edu

## Slide 2: The Black Box of TCP
Packets go in and packets go out
  But what happens in the stack?
    Few mechanisms to observe in real time
    Throughput little better than “Check Engine” light
  Observations are difficult
    Analysis after the fact not as useful as advertised
    Real time observation often incurs significant cost and complexity
  Would knowing more help?
    Yes, depending…

## Slide 3: Opening the Box
Web10G
  Set of 127 instruments conforming to RFC 4898
  Built as patch to Linux kernel
  Includes kernel module and API
TCP_INFO
  Part of the TCP stack (Linux 2.4)
  Contains 38 instruments (Linux 4.2)
  Available as a tcp option via getsockopt

## Slide 4: Web10G
Advantages
  Collects more data of interest (application performance, path characteristics, &c)
  Kernel is aware of MIB and can tell userland what instruments are supported.
  Uses independent memory space in kernel
    Metrics persist after socket close
  API makes working with metrics easy
    Also correlates data to calling application
Disadvantages
  Not in mainline – yet
  Slightly higher memory requirements

## Slide 5: TCP_INFO
Advantages
  Well supported in kernel
  No additional overhead
Disadvantages
  Not well documented
  Smaller instrument set
  Struct is hardcoded
    May not be portable between Linux kernels
  Increases socket memory footprint
    Though this is unavoidable.

## Slide 6: It’s Not About Collecting Data
Gathering data is pointless if we don’t use it.

## Slide 7: Some questions:
What if we could see what is happening in a flow in real/near real time?
What if we could apply advanced heuristics to identify marginal and failing flows?
What if we could use this specifically for large data flows from, to, and between Science DMZs?
What if we could use this to monitor inter-domain traffic across an R&E?

## Slide 8: Answer

## Slide 9: A Better Answer
You’d have XSight

## Slide 10: XSight Overview
Goal: Create a detailed panoptical view of a monitored network on a per flow basis and alert engineers of failing flows while they are happening
Major components
  Listener collects data from the edge of the network and forwards to DB.
    Distributed throughout network on data transfers nodes inside Science DMZs
  Analysis agent reviews data generating alerts for failing flows
  UI provides quick overview of health of flows in monitored region and access to time series data.

## Slide 11: Listener
  Application lives on web10g enabled endpoints
    The more widely distributed the better.
  Periodically polls for new connections & data
  Filters allow for exclusion and inclusion of apps, networks, and individual IPs.
    Can limit to just gridftp or extend to all flows.
  Can create defined groups to send specific network metrics to different databases
    E.g Internal traffic sent to local DB and XSEDE traffic to DB instance at NOC.
  Interfaces with InfluxDB via curl

## Slide 12: Analysis
Analysis is hard
  People have been trying for years and it’s still tough.
However, we have some heuristics
  Use historical data to generate data for macroscopic TCP behaviour model.
  General loss rates, RTT shifts, path changes, stalled applications, etc.
  Collecting path data may allow per segment analysis as well.
Develop what we can to start and use collected data to refine analysis.

## Slide 13: DB & UI
Database
  InfluxDB: Time series optimized NoSQL DB
  Stores metrics, path, application, tuple, and flow start/end times
UI
  Logical map displays network overview allowing users to drill down to find important details.

## Slide 18: Brief Mention
TestRig2.0
  Aimed at providing users with a dynamically generated bootable ISO to automate network testing.
    Uses Web10g to collect information on the evolution of TCP test flows.
    Also used and Web10g enabled version of NDT

## Slide 19: Conclusion
End host TCP stack data is important
It’s also important that you do something with it.
  We have to start building tools that are:
    Real or near real time
    Real world
    Real useful

## Slide 20: Thanks!
rapier@psc.edu
XSight: http://www.nsf.gov/awardsearch/showAward?AWD_ID=1521303
TestRig2.0: http://www.nsf.gov/awardsearch/showAward?AWD_ID=1534836